## Slide 1: Providing Performance Guarantees in Multipass Network Processors
Isaac Keslassy | Kirill Kogan | Gabriel Scalosub | Michael Segal
EE, Technion | CISCO & CSE, BGU | CSE, BGU | CSE, BGU

## Slide 2: Intro to Network Processors (NPs)
Modern routers use network processors for almost everything
  Forwarding
  Classification
  DPI
  Firewalling
  Traffic engineering
Homogeneous tasks and homogeneous traffic
  Classical NP architectures do pretty well
Increasing heterogeneous demands
  Tasks include: VPN encryption, LZS decompression, advanced QoS, …
  Classical NP architectures become sluggish
What are “classical NP architectures”?

## Slide 3: NPs’ Architectures
Pipelined
  each processor (PPE) performs its task in sequence
  main handicaps: hard to extend, synchronous, packet header copy
Parallel/multi-core
  each processor (PPE) performs all tasks until all completed
  main handicap: run-to-completion
Hybrid: pipeline + parallel
Multi-pass
  (control!) packets recycled into the queue after each processing cycle
  main benefits:
    easily extendable, asynchronous
    no run-to-completion (heavy-hitters do not starve light-hitters)
E.g., Xelerated X11 NP
E.g., Cavium CN68XX NP
E.g., CISCO QuantumFlow NP
E.g., EZChip NP-4 NP

## Slide 4: Network Model & Methodology
Abstracting a multi-pass architecture
SM: scheduler module
  Buffer management policy
    Overflows!!!
  Assignment of packets to PPEs
Goal:
  Maximize ( throughput )
Multi-core: C PPEs
  In this talk: focus on C=1
Competitive approach
  c-competitive: for any input sequence σ, A(σ) ≥ OPT(σ) / c
  arbitrary arrival sequences (adversarial…)

## Slide 5: Further Assumptions & Notation
Homogeneous packets
  unit-value
  unit-size
  buffer capacity: B packets
Slotted time
r(p): packet p’s required passes
  known upon packet arrival
  max required passes: k
    need not be known in advance
  residual passes:
    If p is processed at t,
    then rt+1(p) = rt(p)-1

## Slide 6: Further Assumptions & Notation
PPE
Homogeneous packets
  unit-value
  unit-size
  buffer capacity: B packets
Slotted time
r(p): packet p’s required passes
  known upon packet arrival
  max required passes: k
    need not be known in advance
  residual passes:
    If p is processed at t,
    then rt+1(p) = rt(p)-1
2
2
4
5
5
5
1
1
PPE
2
2
4
5
5
5
1
1
1
PQ
(less work = higher priority)
FIFO
1

## Slide 7: Our Focus and Results
Assignment: Work conserving
  no slacking off
Buffer Management : Greedy
  never drop if there’s still room
Assignment of packets to PPEs:
  FIFO
  Priority Queueing (PQ)
Buffer Management:
  preemptive vs. non-preemptive
Implementation cost
  preemption has its cost (e.g., copying)
Competitive Algorithms
&
Lower Bounds
(and simulations)

## Slide 8: A Case for Preemption
FIFO lower bound
  simple traffic pattern: competitive ratio is (k)
PQ lower bound
  (much) more involved
  also (k)
Can preemption help?
  it doesn’t help OPT…
(OR, how bad can non-preemption be when buffer overflows?)
Matching O(k) upper bounds for both

## Slide 9: What If We Preempt?
Preemption rule (p arriving, pmax in the buffer has max rt):
  if r(p) < rt(pmax), drop pmax and accept p
  else drop p
Preemption + PQ = Optimal
  PQ can serve as a benchmark for optimality
    very useful (stay tuned…)
Preemption + FIFO?
  not optimal: (log k) lower bound
  sublinear(k) upper bound: still open

## Slide 10: Are Preemptions Free?
New packets “cost” more than recycled packets
  costly memory access
  system updates (pointers, data-structures)
Copying cost
  each new packet admitted incurs a cost of [0,1)
Objective:
  maximize ( Throughput – Cost )
Observations:
  optimal offline solution never preempts: OPT = (1-)OPTno-cost

## Slide 11: Algorithm PQ
Preemption rule (p arriving, pB last in buffer – has max rt):
  if r(p) < rt(pB) / , drop pB and accept p
  else drop p
 =1:
  PQ  regular preemptive PQ
 =:
  PQ  non-preemptive PQ

## Slide 12: Algorithm PQ
Preemption rule (p arriving, pB last in buffer – has max rt):
  if r(p) < rt(pB) / , drop pB and accept p
  else drop p
Competitive ratio: f(k,,)
What is the best ?
  for each value of k and :
    gk, () =f(k,,)
  minimized for some (k,)
  Knowing k helps… (here, k=100)
(1- ) (1 + log/(-1)(k/2) + log(k))
1-  log(k)

## Slide 13: Simulation Results
Single PPE (C=1), increasing copying cost {0.1,0.4}
  MMPP Traffic (ON-OFF bursty), increasing pass-load
Best algorithm changes
Performance much better than worst-case guarantee

## Slide 14: Summing Up
Model for multi-pass NP architectures
Competitive algorithms & lower bounds
  FIFO vs. PQ
  preemptive vs. non-preemptive
  effect of copying cost
Simulations:
  algorithmic insight is sound
  perform better than worst-case guarantee
Many open questions…

## Slide 15: Questions?